BIDFORM

(Technical Specification)

“FOR ENVELOPE 1”

Bid No. : BAC3-NIHPNEI-PR1920

Date     : July 17, 2017

Unit     : NIH-PNEI

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |

| Supply of Auditory Evoked Potential System with hearing-in-nose test system, screening and portable OAE and audiometer Clinical Purpose: Measuring evoked potentials to assist in evaluation, documentation and diagnosis of hearing disorders in human beings. Test type with software includes: a. Auditory Brainstem Response (ABR) b. Middle Latency Response (MLR) c. Late Latency Response (LLR) d. P300 e. Mismatch Negativity (MMN) f. Electrocochleography (EchochG) g. Cochlear Microphonic (CM) h. Electric Auditory Brainstem Response (eABR) I. Automated Auditory Brainstem Response (AABR) j. Auditory Steady State Response (ASSR) k. Vestibular Evoked Myogenic Potential (VEMP) l. Masking Noise Level (MNL) m. Otoascoutic Emission (DPOAE & TEOAE) |  |  |  |  |
| --- | --- | --- | --- | --- |

BIDFORM

(Technical Specification)

“FOR ENVELOPE 1”

Bid No. : BAC3-NIHPNEI-PR1920

Date     : July 17, 2017

Unit     : NIH-PNEI

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | Stimulus: a. Click b. Tone burst Presentation: a. EEG b. Normative latency c. Latency d. Latency calculation e. Residual noise f. FMP values g. EcochG area Patient Group: Newborn to geriatric Result Evaluation: Manually / subjective Preamplifier: a. 2 channels b. A/D resolution: 16 bit c. with Common mode rejection ratio Shipping weight: 667 lbs. (303kg) |  |  |  |  |

BIDFORM

(Technical Specification)

“FOR ENVELOPE 1”

Bid No. : BAC3-NIHPNEI-PR1920

Date     : July 17, 2017

Unit     : NIH-PNEI

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | Averaging: Standard plus high and low filtering With patient database management system With software for hearing-in-noise-test With connections for soundfield testing/ speakers Narrowband stimuli with automated response detection methods VEMP with visual feedback & ratio calculation AEP System must be delivered with the following accessories: 1 unit Insert earphones 1 unit Supra-aural headphone 1 unit Bone ossilator 1 pack each of ABR insert Eartips (for neonates, infant and adult) 1 pack Standard reusable cup electrodes 2 packs Snap electrode 5 boxes Electrode cable with re-usable electrodes Insert Pre-gelled electrodes Pre-gelled electrodes 2 Tip trode electrode cable sets 20 pcs. Tip trode gold electrodes for ECochG |  |  |  |  |

BIDFORM

(Technical Specification)

“FOR ENVELOPE 1”

Bid No. : BAC3-NIHPNEI-PR1920

Date     : July 17, 2017

Unit     : NIH-PNEI

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | 10 pcs. TM trode gold electrodes 4 tubes Skin preparation gel 2 jar Electrode paste 4 boxes Alcohol pads 4 boxes Gauze swabs Foam Insert Eartips (different sizes for neonate, infant and adult) Extra box of ear foam tips (different sizes for neonate, infant and adult) Extra box of disposable electrodes and gel With cart Portable OAE Specification: Hand-held with carrying bag/ case Power Supply: lithium ion rechargeable Battery Life: minimum of 300 tests Display: LCD or OLED Automatic date and time setting Measurement Type: Distortion Product Otoacoustic Emissions (DPOAE) and/ or Transient Evoked Otoacoustic Emissions (TEOAE) |  |  |  |  |

BIDFORM

(Technical Specification)

“FOR ENVELOPE 1”

Bid No. : BAC3-NIHPNEI-PR1920

Date     : July 17, 2017

Unit     : NIH-PNEI

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | Frequency range: DPAOE: 1.5-12Khz; TEAOE: 0.7 -4 Khz Stimulus Intensity: DPOAE: 40-70dB SPL; TEOAE: 83dB SPL Averaging Time: DPOAE: 0.5-4 seconds; TEAOE: 8-64 seconds Pass SNR (Signal-to-Noise Ration): DPOAE: 6dB; TEOAE: 4 dB Number of Passing Frequencies for Overall Test “Pass”: 3 Portable OAE must be delivered with the following accessories: With Cradle Complete With Database Software With Printer With Thermal Printer Alkaline or Built-in Battery With Probe cables With probe tips for newborns, infants and adults Extra box or ear foam tips With Thermal Printer Paper Rolls Audiometer Specifications: > 12 standard frequencies > NOAH-based software compatible |  |  |  |  |

BIDFORM

(Technical Specification)

“FOR ENVELOPE 1”

Bid No. : BAC3-NIHPNEI-PR1920

Date     : July 17, 2017

Unit     : NIH-PNEI

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | > 2 separate channels > 220 volts power Audiometer must be delivered with the following accessories: a. supra-aural or circum-aural headphone b. insert earphone c. bone ossilator d. carrying case e. patient response button Must be delivered with the following consumables: 1. Disposable eartips for insert earphone a. Small size, 200 pcs. b. Medium size, 200 pcs. c. Large size, 200 pcs. 2. Gauze pads, 2 boxes With Laptop: The specs- or higher, maintaining compatibility with updated system software |  |  |  |  |

BIDFORM

(Technical Specification)

“FOR ENVELOPE 1”

Bid No. : BAC3-NIHPNEI-PR1920

Date     : July 17, 2017

Unit     : NIH-PNEI

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | • 15.6'' (39.62cm) HD (1366x768) 16:9 panel, 3.88m • Intel Core i5-6300HQ Processor (6CM Cache 2.30GHz up to 3.20GHz) (4 Cores and 4 Threads) • Mobile Intel HM170 Express Chipset • 8GB DDR3L 1600MHz So-Dimm System Memory (Operation frequency depends on processor) • Geniune Microsoft Windows 8.1- Professional (64 bit); Upgrade Rights to Windows 10 Professional / Windows 7 (depending on compatibility of machine software) • No application software selected • No M.2 SSD drive selected; M.2 SSD drive configures as an OS Drive (Primary drive C:) • 1 TB Internal SATA hard drive • 8X DVD R/RW/4X + DL Super-Multi drive & software • 2 GB gDDR3 Video RAM NVIDIA GeForce 940M (GPU Switchable between iGPU and dGPUD) • nVIDIA Optimus Technology, nVIDIA PhysX technology, GeForce CUDA technology • Built in high definition audio subsystem |  |  |  |  |

BIDFORM

(Technical Specification)

“FOR ENVELOPE 1”

Bid No. : BAC3-NIHPNEI-PR1920

Date     : July 17, 2017

Unit     : NIH-PNEI

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | • Intel Dual Band Wireless-AC 3160 802, 11ac,a/b/g, N(2,4/5GHz Band: 433 Mbps); Integrated bluetooth 4.0; Supports wireless display 9-in-1 card reader (MMC/RSMMC/SD/mini SD/ SDHC/ SDXC/ MS/MS Pro/MS Duo • U1535 ports: 3 x USB 3.0 ports, 1 x USB 2.0, VGA port, HDMI port, Headphone, microphone port, LAN Port, DC jack • Full range AC adapter, AC in 100│240V, 50│60Hz, DC Output 19V, 4.74A, 90W • Built-in 10/100/1000Mb Base-TX ethernet LAN and Printer: OS Compatibility: Windows 7/8.1 or higher Rated Voltage: AC 220-240V Power Consumption: 12W Paper Feed Method: Friction feed Minimum Ink Droplet Volume: 3 pl Bluetooth/ Wireless Printing Speed: up to 30ppm |  |  |  |  |

BIDFORM

(Technical Specification)

“FOR ENVELOPE 1”

Bid No. : BAC3-NIHPNEI-PR1920

Date     : July 17, 2017

Unit     : NIH-PNEI

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | Printer resolution: up to 6000dpi Cartridge Type: Individual Ink Tanks (4 colors) With USB cable With Power cable With database software With Mouse pad With preamplifier With carrying case With UPS (good for 1 hour); AVR (adequate KVA) Terms and Conditions: 1. Indicate brand, model and country origin. 2. Notarized certificate that the product is brand new, not reconditioned/ refurbished including parts and service. 3. Delivery and installation should be done within sixty (60) calendar days commencing on the 3rd working day of notification through confirmed fax that the approved Purchase Order/ Contract is already available for pick up. 4. The system must be delivered ready to use. Cables, connectors, adapters and accessories not specified but essentials for the unit to function must be |  |  |  |  |

BIDFORM

(Technical Specification)

“FOR ENVELOPE 1”

Bid No. : BAC3-NIHPNEI-PR1920

Date     : July 17, 2017

Unit     : NIH-PNEI

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | provided free by the winning bidder. 5. Certification from at least three (3) government and / or private hospital within Metro Manila or the Philippines that they have been supplies the same brand being offered. 6. Provide product orientation and operations training and trouble shooting training for end users. 7. Warranty and preventive maintenance should be five (5) years and two (2) years on parts. 8. Warranty period shall commence from the date of acceptance by the end-user, testing and commissioning. 9. Provide regular quarterly preventive maintenance and calibration during the warranty period. 10. A notarized certification from the manufacturer that 11. Certification from the manufacturer and local distributor that in the event of a change of local distributor, preventive maintenance, warranty and services agreed here upon will be honored by the principal manufacturer. 12. Certification that the local distributor and the manufacturer have been in business relationship of providing that said equipment for at least three (3) years. |  |  |  |  |

BIDFORM

(Technical Specification)

“FOR ENVELOPE 1”

Bid No. : BAC3-NIHPNEI-PR1920

Date     : July 17, 2017

Unit     : NIH-PNEI

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | 13. Notarized certification accompanied with proof that the bidder is in the business of supplying the unit/ item for the last three (3) years. 14. Guarantee letter or certificate from the manufacturer and local distributor to ensure the availability of parts, supplies and accessories and will not be discontinued for the next five (5) years. 15. Provide separate quotation for maintenance, repair and replacement of parts after warranty period. 16. Must be provide a soft copy (compatible with UPM-PGH Operating System) in CD and hard copy of technical specifications. 17. Provide operator's and service manual upon delivery in English Language. 18. The bidder must submit certification that they have the capability for corrective and preventive maintenance of unit. 19. Must guarantee that diagnostic technician to be able to assess the unit within 24 hours of notification. 20. Automatic provision of a functioning service unit (same model or higher) upon pull out of the purchased unit during the warranty period. 21. Price is inclusive of VAT and all duties |  |  |  |  |