BIDFORM

(Technical Specification)

“FOR ENVELOPE 1”

Bid no. :  BAC3-OVCR-PR2751

Date     :  October 23, 2017

Unit     : Office of the Vice Chancellor for Research

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | Supply and Installation of Network and Power Over Ethernet (POE) Switches (1 Unit) WIFI Access Point Indoor Dual Band 802.11ac 2x2:2 stream MIMO with mounting kit and POE Injector, capable of supporting 500 clients per AP, adaptive antennas and automatic interference mitigation, concurrent dual-band (5Ghz/2.4Ghz) support, beamforming, dual ports, 802.3a PoE support, support for multiple BSSIDs with unique QoS and security policies, Zero-IT and Dynamic PSK, mounting kit for hard wall/ceilling, outlet box, pole, truss; 100% compatible with existing wireless controller used by campus. Must include access point licenses for controller management. |  |  |  |  |

BIDFORM

(Technical Specification)

“FOR ENVELOPE 1”

Bid no. :  BAC3-CM-PR2195

Date     :  September 25, 2017

Unit     : College of Medicine- Dept. of Anatomy

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | General Features: Support 802.11 a/b/g/n/ac functionality certified by the WI-FI alliance. Must be plenum rated with applicable certification. Able to be powered over 802.3af standard Power-Over Ethernet (POE) or 802.3at (POE+). Dual radio 4x4 802.11ac AP with multi-user MIMO. Support 1.7Gbps in 5Ghz band and 800Mbps in 2.4Ghz band Support out of the box, auto configuration across layer 2 and layer 3 networks without having to enter configuration information into the AP. APs do not hold “hard configured” internal network information or certificates for authentication to the centralized switches unless this information is stored in a trusted platform module (TPM) intergrated into the AP. |  |  |  |  |

(Technical Specification)

“FOR ENVELOPE 1”

Bid no. :  BAC3-CM-PR2195

Date     :  September 25, 2017

Unit     : College of Medicine- Dept. of Anatomy

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | Minimum of 16 SSIDs and BSSIds available on each AP Capable of multi-function sevices including: data access, location tracking, real-time non-disruptive packet capture, RF monitoring with no physical “touch” and no additional cost. Support up to 2.5Gbps with Nbase-T compatibility Built-in Bluetooth Low Energy (BLE) radio Two 10/100/1000Base-T with support for link aggregation up to 2Gbps. Support max data-rate of 1.7Gbps in the 5Ghz band and 800Mbps in the 2.4Ghz band. Must include appropriate access point and firewall linceses Warranty & Service Warranty & Service shall include 3 years 8x5 advanced |  |  |  |  |

(Technical Specification)

“FOR ENVELOPE 1”

Bid no. :  BAC3-CM-PR2195

Date     :  September 25, 2017

Unit     : College of Medicine- Dept. of Anatomy

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | Support with NBD Onsite Service including Hardware supports (repair or replacement), firmware updates, configuration and other advanced services for the proposed equipment. All equipment under warranty contract found to be defective should be replaced by the vendor or supplier on the next business day without additional cost to UP Diliman and UP Manila Bidder Qualification Bidder must be authorized Tier 1 (or its equivalent) partner or reseller of the brand they are carrying. Certificate must be issued by Manufacturer local office or its authorized distributor and must be attention to Chairperson, UP Bids and Awards Committee. Bidder must be a network system integrator for at least five (5) years |  |  |  |  |

(Technical Specification)

“FOR ENVELOPE 1”

Bid no. :  BAC3-CM-PR2195

Date     :  September 25, 2017

Unit     : College of Medicine- Dept. of Anatomy

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | In the Philippines and system integrator partner of the proposed brand for the last three (3) years. Bidder must have at least two (2) certified experts/engineers to provide support and implementation. Vendor certification must be provided Responsibility of the Supplier Shall deliver, install, and configure the proposed equipment including all components & software if any within 60 calendar days upon receipt of Notice to Proceed (NTP) Shall provide Project Manager as a point person for issues and concerns about the project and deliverables Shall provide documentation of all the configuration made by the vendor. Shall provide a Knowledge Transfer training on installation, configuration and administration for three (3) IT Support personnel |  |  |  |  |

(Technical Specification)

“FOR ENVELOPE 1”

Bid no. :  BAC3-CM-PR2195

Date     :  September 25, 2017

Unit     : College of Medicine- Dept. of Anatomy

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | It should be 100% compatible with existing wireless controller used by campus Network Attached Storage Specs: Interface: Gigabit Ethernet (10/100/1000 Mbps) No. of Drives: Two (2) Capacity: 8TB RAID: RAID 0, RAID 1 (Mirror Mode) USB: Two USB 3.0 ports Features: Apple Time Machine Backup supported Connection to public clouds, e.g, Dropbox and other public cloud accounts via app Supports Windows and Mac OS X Switch Specs: Item A. Network Switch Layer 3: 48-Port Layer 3 Stackable Gigabit PoE (435W) + Switch (IP Base) Quantity: One (1) Connectors and Cabling: 1000BASE-T ports: RJ-45 connectors, 4-pair Cat-5E UTP cabling 1000BASE-T SFP-based ports: RJ-45 connectors, 4 pair Cat-5E |  |  |  |  |

(Technical Specification)

“FOR ENVELOPE 1”

Bid no. :  BAC3-CM-PR2195

Date     :  September 25, 2017

Unit     : College of Medicine- Dept. of Anatomy

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | UTP cabling 100BASE-FX, 1000BASE-SX, -LX/LH, -ZX, -BX10, DWDM and CWDM SFP transceivers: LC fiber connectors (single mode or multimode fiber) 10GBASE-SR, LR, LRM, CX1 (v02 or higher) SFP+ transceivers: LC fiber connectors (single-mode or multimode fiber) StackPower-480 stacking ports: copper-based Stackwise cabling StackPower: Power stacking cables Ethernet management port: RJ-45 connectors, 4 pair Cat-5 UTP cabling Management console port: RJ-45-to-DB9 cable for PC connections Power Connectors: Customers can provide power to a switch by using either the internal power or StackPower from another member in the power stack. The connectors are located at the back of the switch. Internal power supply connector: The internal power supply is an auto-ranging unit. The internal power supply supports input voltages between 100 and 240VAC. Use the supplied AC power cord to connect the AC power connector to an AC power outlet. |  |  |  |  |

(Technical Specification)

“FOR ENVELOPE 1”

Bid no. :  BAC3-CM-PR2195

Date     :  September 25, 2017

Unit     : College of Medicine- Dept. of Anatomy

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | Standards: IEEE 802.1s IEEE 802.1w IEEE 802.11 IEEE 802.1x IEEE 802.1x-Rev IEEE 802.3ad IEEE 802.3x full duplex on 10BASE-T, 100BASE-TX, and 1000BASE-T ports IEEE 802.1D Spanning Tree Protocol IEEE 802.1p CoS prioritization IEEE 802.1Q VLAN IEEE 802.3 10BASE-T specification IEEE 802.3u 100BASE-TX specification IEEE 802.3ab 1000BASE-T specification IEEE 802.3z 1000BASE-X specification RMON I and II standards SNMPv1, SNMPv2c, and SNMPv3 |  |  |  |  |

(Technical Specification)

“FOR ENVELOPE 1”

Bid no. :  BAC3-CM-PR2195

Date     :  September 25, 2017

Unit     : College of Medicine- Dept. of Anatomy

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | Switch Summary: Stackable 24 10/100/1000 Ethernet ports, with 350 WAC power supply. 1 RU, IP Base feature set Item B. Power-over-Ethernet Switch: Quantity: Five (5) Hardware Summary: Must include rack-mounting kit Size: 1 Rack unit Ports: 4 Fixed 1000 based SFP ports (24) RJ-45 autosensing 10/100/1000 PoE+ ports Should have virtual stacking capability and support 16 switches Available POE Power: At least 195W Performance: Minimum switching capacity 56Gbps Minimum throughput of 41.6Mbps Minimum 1000Mb latency: <2.3ms QoS: Support traffic prioritization (802.1p) – Allows real-time traffic classification with support for eight priority levels mapped to either two of four queues, and uses weighted deficit round robin (WDRR) |  |  |  |  |

(Technical Specification)

“FOR ENVELOPE 1”

Bid no. :  BAC3-CM-PR2195

Date     :  September 25, 2017

Unit     : College of Medicine- Dept. of Anatomy

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | Or strict priority Should support Rate limiting/ L4 prioritization/ Flow Control Management: The switch shall support Telnet, SSH and Zero-Touch provisioning The Switch shall support SNMP1/v2c, and SNMPv3 Should support sFlow (RFC 3176), Virtual stacking, logging and port mirroring The switch must have the following management options: Web GUI and Robust CLI Layer 2 Specifications and Feature: Minimum MAC addresses : 16,600 Jumbo frames: 9,220-byte frame size Number of VLANs: 512 VLANs and 4096 VLAN IDs Maximum active VLANs: 512 GARP VLAN Registration Protocol Rapid Per-VLAN spanning Tree (RPVST+) Support ACL Source-port filtering |  |  |  |  |

(Technical Specification)

“FOR ENVELOPE 1”

Bid no. :  BAC3-CM-PR2195

Date     :  September 25, 2017

Unit     : College of Medicine- Dept. of Anatomy

|  | REQUIRED SPECIFICATIONS | OFFERED SPECIFICATIONS | REFERENCES (include Supporting documents) | COMMENTS/REMARKS (clarify inclusion/ exclusion) | EVALUATION |
| --- | --- | --- | --- | --- | --- |
|  | RADIUS/TACACS+ Secure Sockets Layer (SSL) Port security and MAC address lock out Multiple User Authentication : 802.1x; web-based authentication; MAC based; SSHv2; Secure shell; STP Root guard; STP BPDU port protection; protected port CLI Port trunking and link aggregation; IEEE 802.1s Multiple Spanning Tree; SmartLink IEEE 802.1AB Link Layer Discovery Protocol (LLDP); IP multicast (data driven IGMP); LLDP-MED (Media Endpoint Discovery); PoE and PoE+ allocations; Voice VLAN; Local MAC authentication; HTTP redirect function Power Supply and Dimension: 100V-240V; POE Power 195W WxDxH = 17.40x12.70x1.75 in Weigt = 3.81KG ITEM C. Transceiver Module: Quantity: One (1) Specifications: 1000 base-LX/LH SFP Transceiver module MMF/SMF, 1310nm,DOM |  |  |  |  |